## Slide 1: Strand Road Trial Modelling analysis and Traffic data
05/10/2020

## Slide 2: Traffic Data
Within the area covered by the trial DCC have the following data:-
Cordon count data and classified counts at a number of locations.
Traffic data from the DCC SCATS Traffic Control system
Count of barrier activations at Merrion gates Level crossing
CCTV at a number of locations linked to DCC Traffic Control Centre for real time monitoring of traffic conditions.
Noise monitor on Strand Road
EPA environmental monitor Ringsend Road

## Slide 3
Existing and new CCTV locations
Linked to the DCC 24/7 control centre

## Slide 4
Traffic volumes crossing the canl cordon comparing pre Covid with current situation on a week by week basis.

## Slide 5: Data from Beach Road northbound
Chart: Beech Round Northbound - AM peak hour
| Pre Covid | 19/05/2020 | 26/05/2020 | 02/06/2020 | 09/06/2020 | 16/06/2020 | 23/06/2020 | 30/06/2020 | 07/07/2020 | 18/08/2020 | 25/08/2020 | 01/09/2020 | 08/09/2020
Car | 655 | 221 | 202 | 220 | 281 | 280 | 303 | 300 | 323 | 326 | 328 | 395 | 381
LGV | 66 | 39 | 36 | 50 | 40 | 43 | 42 | 43 | 36 | 32 | 39 | 42 | 42
HGV 2 & 3 Axles | 7 | 4 | 8 | 3 | 11 | 7 | 4 | 2 | 6 | 13 | 4 | 6 | 3
HGV 4+ Axles | 7 | 2 | 4 | 2 | 4 | 2 | 2 | 4 | 5 | 4 | 2 | 1 | 1

## Slide 6
Chart: Northbound v Southbound AM peak hour Cars,LGVS & HGVs
| Pre Covid | 19/05/2020 | 26/05/2020 | 02/06/2020 | 09/06/2020 | 16/06/2020 | 23/06/2020 | 30/06/2020 | 07/07/2020 | 18/08/2020 | 25/08/2020 | 01/09/2020 | 08/09/2020
Northbound | 735 | 266 | 250 | 275 | 336 | 332 | 351 | 349 | 370 | 375 | 373 | 444 | 427
Southbound | 866 | 311 | 370 | 384 | 441 | 435 | 438 | 481 | 498 | 500 | 491 | 594 | 656
Northbound/Southbound comparison

## Slide 7
Strand Road has one of the highest noise readings in the City.

## Slide 8
Information available at dublincityairandnoise.ie

## Slide 9
Taken from SCATS Traffic Control System

## Slide 10: NTA Eastern Regional Model Findings
Recent traffic surveys (Pre-Covid) indicate:
  675 vehs travelling Northbound in AM peak hour at the select link location
    634 cars
    29 LGVs
    12 HGVs
The majority of traffic comes from Merrion Road via Merrion Gates (618 vehs) which is reflected in the Select Link Analysis

## Slide 11
Select Link undertaken NB at this location
AM Peak Hour
The links in Green show both origin and destination of traffic using Strand Road northbound prior to Covid
Merrion Gates

## Slide 12
The modelled split between traffic heading to East Link and the City Centre
East Link
Ringsend
Strand Road
NTA ERM

## Slide 13
Difference of Actual Flow
AM Peak Hour (Current Scenario v Proposed scenario)
Decrease
Increase
 |  | 2020 AM flows (pcu/h) |  | 
 |  | Reference | Do Something | %Diff
Nutley Lane | Northbound | 766 | 699 | -9%
 | Southbound | 562 | 641 | 14%
Park Avenue | Northbound | 162 | 198 | 22%
 | Southbound | 409 | 406 | -1%
Merrion Rd (North of Merrion gate) | Northbound | 371 | 795 | 114%
 | Southbound | 384 | 466 | 21%
Sandymount Rd | Northbound | 488 | 597 | 22%
 | Southbound | 488 | 467 | -4%
Serpentine Av | Northbound | 359 | 490 | 36%
 | Southbound | 208 | 208 | 0%
Sandymount Av | Northbound | 162 | 264 | 63%
 | Southbound | 174 | 183 | 5%
NTA ERM
Merrion Gates
Pre Covid Volumes

## Slide 14
Decrease
Increase
Difference of Actual Flow
AM Peak Hour (Current Scenario v Proposed scenario)
NTA ERM

## Slide 15
Difference of Delay
AM Peak Hour (Current Scenario v Proposed scenario)
Decrease
Increase
NTA ERM
Merrion Gates