## Dodder Greenway

### Fitzwilliam Quay to Londonbridge Road

- Fitzwilliam Quay to Londonbridge Road has been identified as a suitable location for interim measures along the Dodder Greenway corridor. It will provide walking and cycling facilities from Fitzwilliam Quay to Londonbridge Road in advance of the Dodder Greenway project. When complete, the project will deliver high quality walking and cycling facilities along the Dodder River from the sea to the mountains through Dublin City Council, Dún Laoghaire Rathdown County Council and South Dublin County Council.

### Sheet 01 of 02 – Fitzwilliam Quay-Ringsend Road/Bridge Street to Dermot O Hurley Avenue.

The scheme begins at the junction of Fitzwilliam Quay and Ringsend Road / Bridge Street, it is proposed to signalize this junction. A toucan (pedestrian and cyclist crossing) is proposed across Ringsend Road and Fitzwilliam Quay at this junction.

A jug turn will allow cyclists to access the toucan crossing on the north side of Ringsend Road allowing cyclists to turn right onto Fitzwilliam Quay. Pedestrian priority areas are proposed at both ends of the toucan crossings to allow pedestrians and cyclists to cross the junction.

A 3 metre wide two-way cycle track is proposed along the length of Fitzwilliam Quay, on the western side of the road. The cycle track will be located on the existing carriageway with the existing kerb line and height remaining in place.  The cycle track itself will be separated from the roadway carriageway by separator kerbs and will be coloured red.

The existing footpaths and kerb heights on the east and west of Fitzwilliam Quay are largely unaffected except at the junction with Ringsend Road / Bridge Street where it is proposed to build out the footpath to facilitate new tactile paving and pedestrian priority areas at the new toucan crossings.

An existing taxi rank, which is located on the west side of Fitzwilliam Quay approximately 10 metres from the junction with Ringsend Road, will be relocated to the eastern side of Fitzwilliam Quay, approximately 60 metres south of the junction with Ringsend Road.

Existing undesignated car parking spaces on the western side of Fitzwilliam Quay are proposed to be removed to facilitate the two way cycle lane.

Existing parking on the eastern side of Fitzwilliam quay will be retained.

Existing Trees on Fitzwilliam Quay are unaffected

### Sheet 02 of 02 – Dermot O Hurley Avenue to Londonbridge Road.

A 3 metre wide two-way cycle track is proposed along the western side of Dodder Park within the existing green area between the Dodder Park Wall and the Dodder River Wall. The existing footpath will remain with a kerb height separation between the cycle track and the footpath, the cycle track will be coloured red.

Uncontrolled pedestrian crossings with tactile as standard are proposed at locations where pedestrians are required to cross the cycle track such as the entrances to Dodder Park. (33 metres and 113 metres south of the junction with Dermot O’Hurley Avenue).

A grass verge of 0.5m will be retained between the cycle track and the Dodder Park Wall.

A pedestrian priority area is proposed in the area of constrained space at the east side of the Pump house building. Cyclists will be permitted to travel along the east of this stone building in this pedestrian priority area. The existing footpath on the western side of the Pump House is unaffected.

A quiet street which is described as mixing cyclists and vehicles will be provided along the existing low traffic volume road section which links the Pump House Apartments to Londonbridge Road, this will be achieved by way of road markings. Existing footpaths and parking will be unaffected along this section of road way.

The scheme ends at the junction of Londonbridge Road.